## Slide 1: Human-machine interaction through gesture recognition
BSc thesis presentation
By Dmitrii Cucleschin

## Slide 2: Motivation
Communicating underwater can be complicated
  Between the divers
  Between the divers and their devices
  Between the divers and the ground crew
“Traditional” input methods can’t be used
Often, the equipment is bulky and can put diver at risk
Need easier, more natural way to interact with the devices: how about gesture recognition?

## Slide 3: State of the art
Research on natural interactions with robots shows higher emotional feedback (Picture: Robot Aurora to help children with autism)
Gesture control in appliances (Samsung Smart TV, Xbox + Kinect, Myo armband, Leap Motion)
Chinese-American sign language translator
Handpose: fully articulated hand tracking

## Slide 4: Setup
  Kinect v2.0 sensor
  Windows 8+
  EmguCV (OpenCV for C#)
  > 4 GB RAM, USB 3.0 controller
  Kinect should be positioned to minimize the noise
  Only one user is present, located directly in front of the sensor
  View is not obstructed by any object in front of the user
  Hand should be extended in front of the body
  Avoid fast movement (due to the motion blur)

## Slide 5: Gesture set
Static:
Dynamic:

## Slide 6: Frame processing
Initialize multi-source frame reader
Get depth and body frames
Save depth frame to a buffer
Extract relevant joint coordinates and convert them to 2D space

## Slide 7: Hand segmentation
Extract relevant region using Flood Fill
Find center point using maximum value of Distance Transform 2D (If more than one, get closest to Kinect’s approximation)
Draw an inner circle with radius r (No more than n/30 black dots)
Draw an outer circle with R = 1.6 * r

## Slide 8: Finger recognition
Analyze values outside of the outer circle
Detect regions from the remaining pixels
Locate the tip and base of every finger
If a region is too wide, classify it as multiple fingers

## Slide 9: Gesture recognition
Finger number matching
Contour matching
Pair-wise geometric histogram comparison (using Bhattacharyya distance)

## Slide 10: Dynamic gesture recognition
Separate dynamic gestures in two types: Wave and Alternation
Analyze frames stored in the buffer (last ~2 seconds)
Extract features of interest (e.g. gesture recognized, joint positions, etc.)
Check whether these features satisfy any dynamic gesture

## Slide 11: Performance

## Slide 12: Quick demonstration?

## Slide 13: Conclusion
Successfully implemented real-time, quite robust gesture recognition system
Can be easily adapted to a custom gesture set
Modular design allows to swap Kinect for another sensor or tweak logic easily
Success rate for recorded gestures reaches 90+%

## Slide 14: Thank you! Any questions?